## Slide 1: CS 211 - Digital Logic Design 211 عال - تصميم المنطق الرقمي First Term - 1439/1440 Lecture #1
Dr. Hazem Ibrahim Shehata
Assistant Professor
College of Computing and Information Technology

## Slide 2: Teaching Staff
Instructor:
  Hazem Ibrahim Shehata
  Email: hshehata@su.edu.sa
  Lectures: Wednesday 8:00am – 9:50am
  Tutorial/lab: Sunday 1:00pm – 2:50pm
  Office Hours: TBA

## Slide 3: Course Info
Course website:
  http://hshehata.github.io/courses/su/cs211/
Textbook:
  “Digital Fundamentals”, Thomas L. Floyd, 10th Edition, 2009, http://catalogue.pearsoned.co.uk/educator/product/Digital-Fundamentals-Pearson-New-International-Edition-10E/9781292025629.page

## Slide 4: Course Info (Cont.)
Grading
Course Work | Grade Distribution | 
Attendance | 10pt | 60pt
Quizzes | 10pt | 
Assignments | 10pt | 
Midterm Exam (1) | 15pt | 
Midterm Exam (2) | 15pt | 
Final Exam | 40pt | 
Total Points | 100pt | 

## Slide 5: Course Overview
Number Systems, Operations, Codes  Ch. 2
Logic Gates and Boolean Algebra  Ch. 3, 4
Combinational Logic  Ch. 5, 6
Sequential Logic  Ch. 7, 8, 9
Memory  Ch. 10 [Optional!]

## Slide 6: Cedar Logic Simulator
Concepts learned in this course are applied using: Cedar Logic Simulator (or shortly: Cedar LS).
  Open-source digital logic simulator
  Developed for academic purposes.
  Very simple and intuitive user interface.
  Download link:
    https://sourceforge.net/projects/cedarlogic/files/latest/download

## Slide 7: Ch.2: Number Systems, Operations, and Codes

## Slide 8: Decimal Numbers
Position of each digit in a weighted number system is assigned a weight based on the base or radix of that system.
Radix/base of decimal system is 10.
  Ten possible values for each digit: 0, 1, 2, …, 9.
  Example: The number 409.63110
Column weights of decimal numbers are powers of 10:
  … 103 102 101 100. 10-1 10-2 10-3 10-4 …
Radix Point
(Decimal Point)

## Slide 9: Decimal Numbers (Cont.)
Decimal numbers can be expressed as sum of products of each digit times column value for that digit.
Example:
  Express the number 480.5210 as the sum of values of each digit.
Solution:
  480.5210 = (4 x 102) + (8 x 101) + (0 x 100) + (5 x 10-1) + (2 x 10-2)

## Slide 10: Binary Numbers
Digital systems use binary number system.
Radix/base of system is 2.
  Two possible values for each binary digit (know as bit): 0 or 1.
  Example: The number 10010.0012
  Note: Values 0 and 1 can be easily represented in hardware using 2 distinct voltage values: low (e.g., 0 volt) and high (e.g., 5 volt)!
Column weights of decimal numbers are powers of 2:
  … 23 22 21 20. 2-1 2-2 2-3 2-4 …
Binary Point

## Slide 11: Conversion: Binary  Decimal
Method: Sum of weights (Add column values of all of bits that are 1 and discard all of bits that are 0).
Example: Convert 100101.012 to decimal.
Solution: Write column weights  Add weights that correspond to 1’s.
  25 24 23 22 21 20 . 2-1 2-2
  32 16 8 4 2 1 . ½ ¼
  1 0 0 1 0 1 . 0 1
  32 +4 +1 +¼ = 37.2510

## Slide 12: Conversion: Decimal  Binary (Integer)
Method #1: Reverse sum-of-weights (Write down column weights and place 1’s in columns that sum to decimal num.)
Example: Convert 4910 to binary.
Solution: Write down column weights until the last number is larger than the one you want to convert.
  26 25 24 23 22 21 20
  64 32 16 8 4 2 1
  0 1 1 0 0 0 1 = 1100012

## Slide 13: Conversion: Decimal  Binary (Integer)
Method #2: Repeated division-by-2 (divide decimal num. by 2 until quotient is 0. Remainders form binary num.)
Example: Convert 1210 to binary.
Solution:
  12 ÷ 2 = 6 0
  6 ÷ 2 = 3 0
  3 ÷ 2 = 1 1
  1 ÷ 2 = 0 1
1
1
0
0
STOP
Remainder
Quotient

## Slide 14: Conversion: Decimal  Binary (Fraction)
Method: Repeated multiplication-by-2 (multiply fractional results repeatedly by 2. Carries form binary fraction)
Example: Convert 0.312510 to binary.
Solution:
  0.3125 * 2 = 0 .625
  0.625 * 2 = 1 .25
  0.25 * 2 = 0 .5
  0.5 * 2 = 1 .0
0
1
0
1
STOP
Carry
0.
Result

## Slide 15: Counting in Binary
Decimal Number | Binary Number |  |  | 
00 | 0 | 0 | 0 | 0
01 | 0 | 0 | 0 | 1
02 | 0 | 0 | 1 | 0
03 | 0 | 0 | 1 | 1
04 | 0 | 1 | 0 | 0
05 | 0 | 1 | 0 | 1
06 | 0 | 1 | 1 | 0
07 | 0 | 1 | 1 | 1
08 | 1 | 0 | 0 | 0
09 | 1 | 0 | 0 | 1
10 | 1 | 0 | 1 | 0
11 | 1 | 0 | 1 | 1
12 | 1 | 1 | 0 | 0
13 | 1 | 1 | 0 | 1
14 | 1 | 1 | 1 | 0
15 | 1 | 1 | 1 | 1
Using 4 bits, we can represent numbers: 0 : 24-1
Using n bits, we can represent numbers: 0 : 2n-1
Decimal Number | Binary Number |  |  | 
00 | 0 | 0 | 0 | 0
01 | 0 | 0 | 0 | 1
02 | 0 | 0 | 1 | 0
03 | 0 | 0 | 1 | 1
04 | 0 | 1 | 0 | 0
05 | 0 | 1 | 0 | 1
06 | 0 | 1 | 1 | 0
07 | 0 | 1 | 1 | 1
08 | 1 | 0 | 0 | 0
09 | 1 | 0 | 0 | 1
10 | 1 | 0 | 1 | 0
11 | 1 | 0 | 1 | 1
12 | 1 | 1 | 0 | 0
13 | 1 | 1 | 0 | 1
14 | 1 | 1 | 1 | 0
15 | 1 | 1 | 1 | 1

## Slide 16: Reading Material
Floyd, Chapter 2:
  Pages 45 – 54