## Slide 1: CS 211 - Digital Logic Design 211 عال - تصميم المنطق الرقمي First Term - 1439/1440 Lecture #5
Dr. Hazem Ibrahim Shehata
Assistant Professor
College of Computing and Information Technology

## Slide 2: Administrivia
Assignment #1:
  Released on Sunday.
  Due: Sunday, October 7, 2018.
Website: http://hshehata.github.io/courses/su/cs211

## Slide 3: Chapter 2: Logic Gates

## Slide 4: Logic Gates/Circuits
Logic Gate: electronic device implementing a basic logical operation on 1+ binary input and producing 1 binary output.
  Examples:
Logic Circuit: electronic circuit built out of logic gates!
  Each wire carries a single bit represented in terms of voltage level.
    High voltage level (e.g., 5v)  logical 1.
    Low voltage level (e.g., 0v)  logical 0.
  Example:
NOT Gate
AND Gate
OR Gate
High (1)
Low (0)
Low (0)
High (1)
Low (0)

## Slide 5: Inverter (or NOT Gate)
Performs operation called inversion or complementation.
  Takes 1 (single-bit) input, and produces 1 (single-bit) output.
  Output value equals the inverse of input value.
Symbols:

## Slide 6: Operation of Inverter
Possible scenarios:
  Low voltage applied to input  High voltage produced at output
  High voltage applied to input  Low voltage produced at output
Operation can be represented as a Truth Table, that lists all input combinations with the corresponding outputs!
Input | Output
Input | Output
Low (0) | 
High (1) | 
Input | Output
Low (0) | High (1)
High (1) | Low (0)

## Slide 7: Logic Expression of Inverter
Boolean Algebra: is a type of mathematics that uses variables and operators to describe logic circuits.
Boolean expression that describes inverter is:
  If , then
  If , then
Complemented variable is read as: “A bar” or “not A”.

## Slide 8: Timing Diagram of Inverter
Timing Diagram: represents how signals of a logic circuit change over time.
  X-axis  time.
  Y-axis  signals values. Either High (1) or Low (0).
Example:
Low
High
Low
High
Time
Time

## Slide 9: Application of Inverter
Inverters can be used to calculate 1’s complement of binary numbers.
Example: Circuit to produce 1’s comp. of an 8-bit number.

## Slide 10: AND Gate
Performs operation called logical multiplication.
  Takes 2+ inputs, and produces 1 output.
  Output value is High (1) if and only if all inputs are High (1).
  Output value is Low (0) if and only if 1+ inputs are Low (0).
Symbols:

## Slide 11: AND Gate Truth Table
For a 2-input AND Gate:
Note: Number of possible binary input combinations to an -input gate is:  Truth table must have rows!
Inputs |  | Output
Inputs |  | Output
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Inputs |  | Output
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 12: Example: Truth Table for 3-input AND Gate
Inputs |  |  | Output

Inputs |  |  | Output
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
Inputs |  |  | Output
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 13: Logic Expression of AND Gate
In Boolean algebra, AND gate is represented using Boolean multiplication operator  “ ”
  Boolean multiplication is similar to binary multiplication:
  , , ,
Boolean expression for 2-input AND gate is:
  , or
Boolean expression for 3-input AND gate is:
  , or

## Slide 14: Timing Diagram of AND Gate
Example: 2-input AND Gate

## Slide 15: Application of AND Gate
Example: Seat Belt Alarm System

## Slide 16: OR Gate
Performs operation called logical addition.
  Takes 2+ inputs, and produces 1 output.
  Output value is High (1) if and only if 1+ inputs are High (1).
  Output value is Low (0) if and only if all inputs are Low (0).
Symbols:

## Slide 17: OR Gate Truth Table
For a 2-input OR Gate:
Inputs |  | Output
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Inputs |  | Output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 18: Example: Truth Table for 3-input OR Gate
Inputs |  |  | Output
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 

Inputs |  |  | Output
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 19: Logic Expression of OR Gate
In Boolean algebra, OR gate is represented using Boolean addition operator  “ ”
  Boolean addition differs from binary addition in one case (1+1=?):
    , , ,
Boolean expression for 2-input AND gate is:
Boolean expression for 3-input AND gate is:

## Slide 20: Timing Diagram of OR Gate
Example: 2-input OR Gate

## Slide 21: Application of OR Gate
Example: Simplified Intrusion Detection System

## Slide 22: NAND Gate
Contraction of NOT-AND  AND with an inverted output.
  Takes 2+ inputs, and produces 1 output.
  Output value is Low (0) if and only if all inputs are High (1).
  Output value is High (1) if and only if 1+ inputs are Low (0).
Symbols:
Equivalent to:

## Slide 23: NAND Gate Truth Table
For a 2-input NAND Gate:
Note: NAND Gate is equivalent to Negative-OR Gate.
Inputs |  | Output
Inputs |  | Output
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Inputs |  | Output
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 24: Logic Expression of NAND Gate
In Boolean algebra, NAND gate is represented by multiplication combined with complementation  “ ”
Boolean expression for 2-input NAND gate is:
  , or
Boolean expression for 3-input NAND gate is:
  , or

## Slide 25: Timing Diagram of NAND Gate
Example: 2-input NAND Gate

## Slide 26: NOR Gate
Contraction of NOT-OR  OR with an inverted output.
  Takes 2+ inputs, and produces 1 output.
  Output value is Low (0) if and only if 1+ inputs are High (1).
  Output value is High (1) if and only if all inputs are Low (0).
Symbols:
Equivalent to:

## Slide 27: NOR Gate Truth Table
For a 2-input NOR Gate:
Note: NOR Gate is equivalent to Negative-AND Gate.
Inputs |  | Output
Inputs |  | Output
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Inputs |  | Output
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 28: Logic Expression of NOR Gate
In Boolean algebra, NOR gate is represented by addition combined with complementation  “ ”
Boolean expression for 2-input NOR gate is:
Boolean expression for 3-input NOR gate is:

## Slide 29: Timing Diagram of NOR Gate
Example: 2-input NOR Gate

## Slide 30: Reading Material
Floyd, Chapter 3:
  Pages XX - XX