## Slide 1: CS 211 - Digital Logic Design 211 عال - تصميم المنطق الرقمي First Term - 1439/1440 Lecture #2
Dr. Hazem Ibrahim Shehata
Assistant Professor
College of Computing and Information Technology

## Slide 2: Administrivia
Course website:
  Up and running but not fully functional yet!!
  URL: http://hshehata.github.io/courses/su/cs211/

## Slide 3: Hexadecimal Numbers
Radix/base of system is 16.
  Sixteen possible values for each digit: 0, 1, 2, …, 9, A, B, C, D, E, F.
  Example: The number 3D57.F0E16
Column weights of hexadecimal num’s are powers of 16:
  … 163 162 161 160. 16-1 16-2 16-3 16-4 …
1010
1210
1410
1110
1310
1510

## Slide 4: Conversion: Hexadecimal  Decimal
Method: Sum of weights
Example: Convert 3FA.416 to decimal.
Solution:
  162 161 160 . 16-1
  256 16 1 . 1/16
  3 F A . 4
  768 +240 +10 +0.25 = 1018.2510
*
*
*
*

## Slide 5: Conversion: Decimal  Hexadecimal
Method:
  Repeated division-by-16 (for integer)
  Repeated multiplication-by-16 (for fraction)
Example: Convert 94310 to Hexadecimal.
Solution:
  943 ÷ 16 = 58 15
  58 ÷ 16 = 3 10
  3 ÷ 16 = 0 3
3
A
F
STOP
Remainder
Quotient

## Slide 6: Conversion: Binary  Hexadecimal
Method: 4-bit grouping (Break binary num. into 4-bit groups starting from radix point; replace each 4-bit group with the equivalent hexadecimal symbol)
Example: Convert 10011101010.1011112 to hexadecimal.
Solution:
  0100 1110 1010 . 1011 1100
  4 E A . B C = 4EA.BC16
  NOTE: A zero added to the right of a fraction or the left of an integer, doesn’t change its value!!

## Slide 7: Conversion: Hexadecimal  Binary
Method: 4-bit replacement (Replace each hexadecimal symbol with the appropriate four bits)
Example: Convert 2B9.3A16 to binary.
Solution:
  2 B 9 . 3 A =
  0010 1011 1001 . 0011 1010 = 1010111001.00111012
  NOTE: A zero removed from the right of a fraction or the left of an integer doesn’t change its value!!

## Slide 8: Octal Numbers
Radix/base of system is 8.
  Eight possible values for each digit: 0, 1, 2, …, 7.
  Example: The number 2407.3218
Column weights of octal numbers are powers of 8:
  … 83 82 81 80. 8-1 8-2 8-3 8-4 …

## Slide 9: Conversion: Octal  Dec./Hex./Bin.
Methods are similar to hexadecimal; with few changes.
  Octal  decimal: sum of weights
  Decimal  octal: repeated division-by-8 and repeated multiplication-by-8
  Binary  octal: 3-bit grouping
  Octal  binary: 3-bit replacement

## Slide 10: Conversion Methods Summary
 | Decimal | Binary | Octal | Hexadecimal
Decimal | - | Repeated Div./Mult. By 2 | Repeated Div./Mult. By 8 | Repeated Div./Mult. By 16
Binary | Sum of Weights | - | 3-bit Grouping | 4-bit Grouping
Octal | Sum of Weights | 3-bit Replacement | - | Oct.  Bin. Bin.  Hex.
Hexadecimal | Sum of Weights | 4-bit Replacement | Hex.  Bin. Bin.  Oct. | -
From
To

## Slide 11: Unsigned Binary Addition
Eight basic rules for adding binary digits (bits):
Example:
When there is no carry (or a carry of 0) | When there is a carry of 1
0 + 0  Sum = 0, carry = 0 | 1 + 0 + 0  Sum = 1, carry = 0
0 + 1  Sum = 1, carry = 0 | 1 + 1 + 0 = 10  Sum = 0, carry = 1
1 + 0  Sum = 1, carry = 0 | 1 + 0 + 1 = 10  Sum = 0, carry = 1
1 + 1  Sum = 0, carry = 1 | 1 + 1 + 1  Sum = 1, carry = 1
+
0
0
1
1
1
1
0
1
0
1
1
0
0
1
1
0
1
1
1

## Slide 12: Unsigned Binary Subtraction
Eight basic rules for subtracting binary digits (bits):
Example:
When there is no borrow (or a borrow of 0) | When there is a borrow of 1
0 – 0  sum = 0, borrow = 0 | 0 – 0 – 1  sum = 1, borrow = 1
0 – 1  sum = 1, borrow = 1 | 0 – 1 – 1  sum = 0, borrow = 1
1 – 0  sum = 1, borrow = 0 | 1 – 0 – 1  sum = 0, borrow = 0
1 – 1  sum = 0, borrow = 0 | 1 – 1 – 1  sum = 1, borrow = 1
–
1
0
1
1
1
0
1
1
0
0
0
1
1
0
1
0
1
1
1

## Slide 13: Unsigned Binary Multiplication
Four basic rules for multiplying binary digits (bits):
  0 × 0 = 0, 0 × 1 = 0, 1 × 0 = 0, 1 × 1 = 1
Example:
1
1
1
0
0
1
1
1
×
0
1
1
1
0
0
0
0
0
1
1
1
0
1
1
1
1
1
1
0
0
1
0
0
+
+
+
Multiplicand
Multiplier
Product
Partial
Products

## Slide 14: Unsigned Binary Division
Same procedure as decimal division  Long Division
Example:
0
1
1
0
0
0
1
1
0
1
1
1
1
1
0
1
0
0
1
1
0
1
0
1
1
1
0
0
1
1
1
1
0
1
1
1
0
0
0
0
1
1
1
0
1
0
0
0
Dividend
Divisor
Remainder
Partial
Remainders
Quotient

## Slide 15: Reading Material
Floyd, Chapter 2:
  Pages 54 – 57
  Pages 72 – 82