## Slide 1: CS 211 - Digital Logic Design 211 عال - تصميم المنطق الرقمي First Term - 1439/1440 Lecture #3
Dr. Hazem Ibrahim Shehata
Assistant Professor
College of Computing and Information Technology

## Slide 2: Administrivia
  Course website:
    http://hshehata.github.io/courses/su/cs211/

## Slide 3: Complements of Binary Numbers
1’s complement:
  Definition: 1’s complement of xxx…xxx2 = 111…1112 – xxx…xxx2.
  = (2n – 1)10 – xxx…xxx2.
  Meaning: Value that complements xxx…xxx2 to 111…1112.
  Method: Flip each bit in the binary number, i.e., (1  0, 0  1).
  Example: What is the 1’s complement of 110100012?
  Solution:
1
1
0
0
0
1
1
0
0
0
0
1
1
1
1
0

## Slide 4: Complements of Binary Numbers
2’s complement:
  Definition: 2’s complement of xxx…xxx2 = 1000…0002 – xxx…xxx2.
  = (2n )10 – xxx…xxx2
  = 1’s complement + 1.
  Meaning: Value that complements xxx…xxx2 to 1000…0002.

## Slide 5: Complements of Binary Numbers
2’s complement (Cont.):
  ...
  Method #1: (1) Find 1’s complement, and then add 1 to it!
  Example: What is the 2’s complement of 100110002?
  Solution:
1
0
0
0
1
1
1
0
1
0
0
0
1
1
0
1
1
+
5
0
1
1
0
1
0
0
0

## Slide 6: Complements of Binary Numbers
2’s complement (Cont.):
  ...
  Method #2: Flip all bits to the left of the least significant 1.
  Example: What is the 2’s complement of 100110002?
  Solution:
1
0
0
0
1
1
1
0
1
0
0
1
0
0
0
0
6

## Slide 7: Signed Numbers
Signed numbers refer to: positive and negative integers.
Represented in digital systems (using bits) in 1 of 3 forms:
  Sign-magnitude, 1’s complement, or 2’s complement.
  Most significant (i.e., left-most) bit represents the sign  sign bit.
    Sign bit = 0  positive number
    Sign bit = 1  negative number

## Slide 8: Signed Number Representation
 | Sign-magnitude | 1’s Complement | 2’s Complement
Positive Numbers +xxx…xxx2 | 0 for sign bit followed by magnitude 0xxx…xxx2 |  | 
 | Sign-magnitude | 1’s Complement | 2’s Complement
Positive Numbers +xxx…xxx2 | 0 for sign bit followed by magnitude 0xxx…xxx2 |  | 
Negative Numbers -xxx…xxx2 | 1 for sign bit followed by magnitude 1xxx…xxx2 | 1’s complement of corresponding +ve number 1’s of 0xxx…xxx2 | 2’s complement of corresponding +ve number 2’s of 0xxx…xxx2
 | Sign-magnitude | 1’s Complement | 2’s Complement
Positive Numbers +xxx…xxx2 | 0 for sign bit followed by magnitude 0xxx…xxx2 |  | 
Negative Numbers -xxx…xxx2 | 1 for sign bit followed by magnitude 1xxx…xxx2 | 1’s complement of corresponding +ve number 1’s of 0xxx…xxx2 | 2’s complement of corresponding +ve number 2’s of 0xxx…xxx2
Range n bits | -(2n-1-1)  2n-1-1 | -(2n-1-1)  2n-1-1 | -(2n-1-1)  2n-1

## Slide 9: Conversion: Decimal  Signed (Ex.)
Example: Represent +1210 and -1210 using 6 bits in the sign-magnitude, 1’s complement, 2’s complement forms.
Solution:
  In binary 1210  001100
 | S-M | 1’s | 2’s
+12 | 001100 | 001100 | 001100
 | S-M | 1’s | 2’s
+12 | 001100 | 001100 | 001100
-12 | 101100 | 110011 | 110100

## Slide 10: Conversion: Signed  Decimal (Ex.)
Example: Which decimal number is represented by the signed value 1011102?
Solution:
  Sign bit = 1  decimal number is negative!
    S-M Form  Number = - 011102 = -1410
    1’s Comp. Form  Number = - (1’s of 1011102) = - 010001 = -1710
    2’s Comp. Form Number = - (2’s of 1011102) = - 010010 = -1810

## Slide 11: Representations of 4-Bit Signed Integers
Decimal
+8
+7
+6
+5
+4
+3
+2
+1
+0
-0
-1
-2
-3
-4
-5
-6
-7
-8
Range of integers that can be represented by 4 bits:
S-M  -7 : +7
 -(24-1-1) : 24-1-1
1’s  -7 : +7
 -(24-1-1) : 24-1-1
2’s  -8 : +7
 -24-1 : 24-1-1
Decimal | S-M
+8 | -
+7 | 0111
+6 | 0110
+5 | 0101
+4 | 0100
+3 | 0011
+2 | 0010
+1 | 0001
+0 | 0000
-0 | 1000
-1 | 1001
-2 | 1010
-3 | 1011
-4 | 1100
-5 | 1101
-6 | 1110
-7 | 1111
-8 | -
Decimal | S-M | 1’s
+8 | - | -
+7 | 0111 | 0111
+6 | 0110 | 0110
+5 | 0101 | 0101
+4 | 0100 | 0100
+3 | 0011 | 0011
+2 | 0010 | 0010
+1 | 0001 | 0001
+0 | 0000 | 0000
-0 | 1000 | 1111
-1 | 1001 | 1110
-2 | 1010 | 1101
-3 | 1011 | 1100
-4 | 1100 | 1011
-5 | 1101 | 1010
-6 | 1110 | 1001
-7 | 1111 | 1000
-8 | - | -
Decimal | S-M | 1’s | 2’s
+8 | - | - | -
+7 | 0111 | 0111 | 0111
+6 | 0110 | 0110 | 0110
+5 | 0101 | 0101 | 0101
+4 | 0100 | 0100 | 0100
+3 | 0011 | 0011 | 0011
+2 | 0010 | 0010 | 0010
+1 | 0001 | 0001 | 0001
+0 | 0000 | 0000 | 0000
-0 | 1000 | 1111 | -
-1 | 1001 | 1110 | 1111
-2 | 1010 | 1101 | 1110
-3 | 1011 | 1100 | 1101
-4 | 1100 | 1011 | 1100
-5 | 1101 | 1010 | 1011
-6 | 1110 | 1001 | 1010
-7 | 1111 | 1000 | 1001
-8 | - | - | 1000

## Slide 12: Signed Addition (2’s Complement)
Addition of 2’complement signed numbers is similar to addition in unsigned binary with two exceptions:
  Final carry bit must be discarded!
  Overflow can happen  Result is incorrect, when:
    Added numbers are positive yet result is negative!!
    Added numbers are negative yet result is positive!!

## Slide 13: Signed Addition (2’s Complement) (Ex.)
Example:
00000111
00000100
00001011
7
4
+
+
11
00001111
11111010
00001011
15
-6
+
+
9
1
00010000
11101000
11111000
16
-24
+
+
-8
11111011
11110111
11110010
-5
-9
+
+
-14
1
01111101
00111010
10110111
125
58
+
+
183
‭10110000‬
‭11001001‬
01111001
-80
-55
+
+
-135
1
Discard!
Discard!
Overflow!
Overflow!

## Slide 14: Signed Subtraction (2’s Complement)
Transformed into addition by the following rule:
  x – y = x + (-y) = x + 2’s complement of y
Example:
11100111
11110100
11110011
-25
-12
–
–
-13
11100111
00001100
-25
12
+
+

## Slide 15: Signed Multiplication (2’s Complement)
Performed in three steps:
  Transform multiplicand and multiplier into positive numbers.
  Perform unsigned multiplication.
  Adjust the sign of product if needed!
    Leave product positive if multiplicand and multiplier signs are similar.
    Negate product (taking its 2’s complement) if multiplicand and multiplier signs are different.

## Slide 16: Signed Division (2’s Complement)
Performed in three steps:
  Transform dividend and divisor into positive numbers.
  Perform unsigned division.
  Adjust the sign of quotient and remainder if needed!
    Leave quotient positive if dividend and divisor signs are similar.
    Negate quotient (taking its 2’s complement) if dividend and divisor signs are different.
    Leave remainder positive if dividend is positive.
    Negate remainder (taking its 2’s complement) if dividend is negative.

## Slide 17: Reading Material
Floyd, Chapter 2:
  Pages 58 - 63
  Pages 66 - 72