## Slide 1
CSE 321a
Computer Organization (1)
تنظيم الحاسبات (1)
3rd year, Computer Engineering
Fall 2016
Lecture #1
Dr. Hazem Ibrahim Shehata
Dept. of Computer & Systems Engineering
Credits to Dr. Ahmed Abdul-Monem Ahmed for the slides

## Slide 2: Teaching Staff
Instructor:
  Hazem Ibrahim Shehata
  Email: hshehata@uwaterloo.ca
  Lectures: Tuesday 10:15am – 12:45am
  Office Hours: TBA
Teaching Assistant:
  Hisham Abdullah
  Email: eng_hisham22@yahoo.com
  Tutorials: TBA
  Office Hours: TBA

## Slide 3: Course Info
Course website:
  http://hshehata.github.io/courses/zu/cse321a/
Textbook:
  “Computer Organization and Architecture: Designing for Performance”, William Stallings, 9th Edition, 2013, www.williamstallings.com/ComputerOrganization

## Slide 4: Course Info (Cont.)
Grading:
Course work | Grade distribution | 
Participation | 3pt | 30
Assignments | 12pt | 
Midterm Exam | 15pt | 
Final Exam | 70pt | 
Total Points | 100 | 

## Slide 5: Course Overview
Ch. 1: Introduction
Ch. 2: Computer Evolution and Performance
Ch. 3: A Top-Level View of Computer Function and Interconnection
Ch. 4: Cache Memory
Ch. 12: Instruction Sets: Characteristics and Functions
Ch. 13: Instruction Sets: Addressing Modes and Formats
Ch. 14 or 19: Processor Structure and Function or Control Unit Operation

## Slide 6: Ch. 1: Introduction

## Slide 7: Organization vs. Architecture (1)
Architecture: attributes visible to the programmer.
  Instruction set, number of bits used for data representation, I/O mechanisms, addressing techniques.
  Ex.: Is there a multiply instruction?
Organization: how features are implemented. Such details may be hidden from programmer.
  Control signals, interfaces, memory technology, number of cores.
  Ex.: Is there a hardware multiply unit or is it done by repeated addition?

## Slide 8: Organization vs. Architecture (2)
All Intel x86 family share the same basic architecture.
This gives code compatibility, at least backwards.
Organization differs between different versions (e.g., Core i3/i5/i7, Xeon, Atom, … etc.)

## Slide 9: Hardware Structure vs. Function
Structure: the way in which components relate to each other.
Function: the operation of individual components as part of the structure

## Slide 10: Structure - Top level
Computer
Main
Memory
Input
Output
Systems
Interconnection
Peripherals
Communication
lines
Central
Processing
Unit
Computer

## Slide 11: Structure - CPU
Computer
Arithmetic
and
Login Unit
Control
Unit
Internal CPU
Interconnection
Registers
Memory
CPU
I/O
System
Bus
CPU

## Slide 12: Structure – Control Unit
CPU
Control
Memory
Control Unit
Registers and
Decoders
Sequencing
Logic
Control
Unit
ALU
Registers
Internal
Bus
Control Unit

## Slide 13: Function
All computers have the following functions:
  Data storage
  Date processing
  Data movement
  Control

## Slide 14: Functional View of a Computer
Data
Movement
Apparatus
Control
Mechanism
Data
Storage
Facility
Data
Processing
Facility

## Slide 15: Data Movement
e.g., keyboard to screen.
Data
Movement
Apparatus
Control
Mechanism
Data
Storage
Facility
Data
Processing
Facility

## Slide 16: Storage
e.g., Internet download to a disk.
Data
Movement
Apparatus
Control
Mechanism
Data
Storage
Facility
Data
Processing
Facility

## Slide 17: Data Processing to/from Storage
e.g., updating a bank statement.
Data
Movement
Apparatus
Control
Mechanism
Data
Storage
Facility
Data
Processing
Facility

## Slide 18: Data Processing from Storage to I/O
e.g., printing a bank statement.
Data
Movement
Apparatus
Control
Mechanism
Data
Storage
Facility
Data
Processing
Facility

## Slide 19: Chapter 2: Computer Evolution and Performance

## Slide 20: Performance Assessment
Factors considered in evaluating processors:
  Cost, size, power consumption, …, and performance.
Performance: amount of work done over time.
Time measurement is straightforward!
  seconds, minutes, hours, … etc.
Work measurement is system-specific!
  # of tasks performed, # of products completed, # of things done … etc.
Ex.: Car assembly line:
  Performance = number of cars assembled every hour.

## Slide 21: Processor Performance
Processor performance is reflected by:
  Instructions-per-second (IPS) rate (Ri): number of instructions executed each second. When instructions are count in millions, this becomes MIPS rate (Rm).
  Programs-per-second (PPS) rate (Rp): number of programs executed each second.
Processor performance parameters:
  Clock speed (f) (in cycles/second or Hz)
    Processor goes through multiple steps to execute each instruction.
    Each step takes one clock cycle to be performed.
    Duration of each clock cycle (cycle time τ) = 1/f

## Slide 22: Processor Performance Parameters
Processor performance parameters (Continued):
  Instruction count (Ic) (in instructions)
    Number of machine instructions executed for a given program to run from start until completion.
  Cycles per instruction (CPI) (in cycles/instruction)
    Number of clock cycles taken to execute an instruction.
    Different types of instructions have different CPI values!
    Average CPI for a program with n different types of instructions:
      Ic: instruction count for the program.
      Ix: number of instructions of type x.
      CPIx: CPI for instructions of type x.

## Slide 23: Performance Metrics
Av. time to execute instruction:
IPS rate:
MIPS rate:
Av. time to execute program:
PPS rate:

## Slide 24: Performance Calculation Example
A 2-million instruction program is executed by 400-MHz processor.
Program has 4 types of instructions:
CPI = (1 * 0.60) + (2 * 0.18) +
(4 * 0.12) + (8 * 0.10) = 2.24
Rm = (400 * 106) / (2.24 * 106) ≈ 178
Rp = (400 * 106) / (2.24 * 2 * 106) ≈ 89
Instruction Type | CPI | Instruction Mix (%)
Arithmetic and logic | 1 | 60
Load/store (Cache hit) | 2 | 18
Branch | 4 | 12
Load/store (Cache miss) | 8 | 10

## Slide 25: Benchmarking
Ri and Rm can’t be used to compare performance of processors with different instruction sets!
  Ex.: CISC vs. RISC
Alternative: Compare how fast processors execute a standard set of benchmark programs.
Characteristics of a benchmark program:
  Written in high-level language (i.e., machine independent).
  Representing different programming styles and applications.
  Measured easily.
  Widely distributed.

## Slide 26: SPEC benchmarks
Best known collection of benchmark suites is introduced by the System Performance Evaluation Corporation (SPEC).
Examples of SPEC benchmark suites:
  SPECcpu2006: 3-million lines of code of processor-intensive applications
    SPECint2006: 12 integer programs (C and C++)
    SPECfp2006: 19 floating-point programs (C, C++ & Fortran).
  SPECjvm2008: java virtual machine
  SPECsfs2014: file server
  SPECweb2009: web server – no longer maintained!
  SPECmail2009: mail server – no longer maintained!
  …

## Slide 27: SPEC Speed Metric (rg)
SPEC defines a base runtime (Trefx) for each benchmark program x using a reference machine.
Runtime of system-under-test (Tsutx) is measured.
Result of running benchmark program x on system-under-test is reported as a ratio (rx):
Overall result of running n-program benchmark suite is the geometric mean (rg) of all ratios:

## Slide 28: Ex.: SPECint2006 on Sun Blade 6250
Sun Blade 6250: 8 processors (2 chips * 4 cores)
Benchmark program 464.h264ref (Video encoding):
  Trefx = 22135s, Tsutx = 934s  rx = 22135/924 = 23.7
Ratios of all SPECint2006 benchmark programs:
Speed metric (rg):
  rg = (17.5 * 14 * 13.7 * … * 14.7)1/12 = 18.5

## Slide 29: Amdahl’s Law
Proposed by Gene Amdahl in 1967.
Deals with potential speedup of a program execution by multiple processors.
Speedup: ratio between program execution time on single processor to that on N processors.
Amdahl’s law: if a program takes time T to be executed by a single processor, and only a fraction f of that program can be executed in parallel using N processors, Then:

## Slide 30: Conclusions of Amdahl’s Law
Amdahl’s law has two important conclusions:
  Parallel processors has little effect when f is small!
    When f goes to 0, speedup goes to 1.
  Speedup is bound by 1/(1–f) regardless of N!
    When N goes to ∞, speedup goes to 1/(1–f).
Amdahl’s law can be generalized to deal with any system enhancements.
Generalized Amdahl’s law: if an enhancement speeds up execution of a program fraction f by a factor k, then:

## Slide 31: Amdahl’s Law for Multiprocessors

## Slide 32: Reading Material
Stallings, Chapter 1:
  Pages 7 – 13
Stallings, Chapter 2:
  Pages 49 – 57