## Slide 1: CS 211 - Digital Logic Design 211 عال - تصميم المنطق الرقمي First Term - 1439/1440 Lecture #6
Dr. Hazem Ibrahim Shehata
Assistant Professor
College of Computing and Information Technology

## Slide 2: Administrivia
Assignment #1:
  Due: Today.
  Solution to be posted tomorrow.
Midterm #1:
  Date: Wednesday, October 24, 2018.
  Time: 8:30am - 9:30am
  Scope: Chapters 2 and 3 (Lectures 1,2,3,4,5, and half-of-6).
Website: http://hshehata.github.io/courses/su/cs211

## Slide 3: Chapter 3: Logic Gates (... Continuing …)

## Slide 4: Exclusive-OR (XOR) Gate
Performs operation called modulo-2 addition, which is the same as binary addition with no carry.
  Takes 2+ inputs, and produces 1 output.
  Output is High (1) if and only if number of High (1) inputs is odd.
  Output is Low (0) if and only if number of High (1) inputs is even.
Symbols:

## Slide 5: XOR Gate Truth Table
For a 2-input XOR Gate:
Inputs |  | Output
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Inputs |  | Output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 6: Example: Truth Table for 3-input XOR Gate
Inputs |  |  | Output
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 

Inputs |  |  | Output
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 7: Timing Diagram of XOR Gate
Example: 2-input XOR Gate

## Slide 8: Application of XOR Gate
Example: 1-bit Modulo-2 adder
+
+
+
+

## Slide 9: Exclusive-NOR (XNOR) Gate
XOR with an inverted output.
  Takes 2+ inputs, and produces 1 output.
  Output is Low (0) if and only if number of High (1) inputs is odd.
  Output is High (1) if and only if number of High (1) inputs is even.
Symbols:
Equivalent to:

## Slide 10: XNOR Gate Truth Table
For a 2-input XNOR Gate:
Inputs |  | Output
Inputs |  | Output
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Inputs |  | Output
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 11: Example: Truth Table for 3-input XNOR Gate
Inputs |  |  | Output
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 

Inputs |  |  | Output
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 12: Timing Diagram of XNOR Gate
Example: 2-input XNOR Gate

## Slide 13: Application of XNOR Gate
Example: 1-bit Binary Comparator
=
≠
=
≠

## Slide 14: Chapter 4: Boolean Algebra and Logic Simplification

## Slide 15: Basic Boolean Terms
Boolean Algebra (BA): the mathematics of digital logic.
Basic terms in BA: Variable, Complement, Literal.
  Variable: symbol (usually an italic uppercase letter or word) to represent an action, a condition, or data. Any single variable can have only a 1 or a 0 value. Example: or .
  Complement: the inverse of a variable and is indicated by a bar over the variable (overbar). Example: or .
  Literal: variable or complement of a variable. Example: or .

## Slide 16: Boolean Addition
Boolean addition () is equivalent to OR operation.
Sum term: sum of literals.
  Produced in logic circuits by OR operation with no AND’s involved.
  Equals 1 if 1+ literals equals 1. Equals 0 if all literals equal 0.
  Examples: ,

## Slide 17: Boolean Multiplication
Boolean multiplication () is equivalent to AND operation.
Product term: product of literals.
  Produced in logic circuits by AND operation with no OR’s involved.
  Equals 1 if all literals equal 1. Equals 0 if 1+ literals equals 0.
  Examples: ,

## Slide 18: Laws and Rules of Boolean Algebra
Commutative Laws (, )
Associative Laws (, )
Distributive Law
Rules of Boolean Algebra (12 rules)

## Slide 19: Commutative Laws
Commutative law of addition:
Commutative law of multiplication:

## Slide 20: Associative Laws
Associative law of addition:
Associative law of multiplication:

## Slide 21: Distributive Law
Distributive Law:

## Slide 22: Rules of Boolean Algebra
Rule 1:
Rule 2:

## Slide 23: Rules of Boolean Algebra
Rule 3:
Rule 4:

## Slide 24: Rules of Boolean Algebra
Rule 5:
Rule 6:

## Slide 25: Rules of Boolean Algebra
Rule 7:
Rule 8:

## Slide 26: Rules of Boolean Algebra
Rule 9:
Rule 10:
  Proof:
    L.H.S. = [R4]
    = [Dist. Law]
    = [R2]
    = [R4]
    = R.H.S.

## Slide 27: Rules of Boolean Algebra
Rule 11:
  Proof:
    L.H.S. = [R10] = [Dist. Law]
    = [R6] = [R4] = R.H.S.

## Slide 28: Rules of Boolean Algebra
Rule 12:
  Proof:
    L.H.S. = [Dist. Law]
    = [R7]
    = [Dist. Law]
    = [R2]
    = [R4]
    = [Dist. Law]
    = [R2]
    = [R4]
    = R.H.S.

## Slide 29: Rules of Boolean Algebra
Rule 12: (…Continuing…)
  Proof:

## Slide 30: Rules of Boolean Algebra - Summary

## Slide 31: Reading Material
Floyd, Chapter 3:
  Pages 130 - 134
Floyd, Chapter 4:
  Pages 172 - 179