## Slide 1
CSE 321a
Computer Organization (1)
تنظيم الحاسبات (1)
3rd year, Computer Engineering
Fall 2017
Lecture #3
Dr. Hazem Ibrahim Shehata
Dept. of Computer & Systems Engineering
Credits to Dr. Ahmed Abdul-Monem Ahmed for the slides

## Slide 2: Administrivia
Office Hours:
  Sunday 1:00pm – 2:00pm
Tutorials:
  Day/Time: Tuesday 8:30am – 10:00am.
Assignment #1:
  Released: by the end of this week.
  Due on: by the end of next week.
  Work in groups of two.
Academic integrity:
  Copying assignments will not be tolerated.
  Involved groups get 0 points!!
Website: http://hshehata.github.io/courses/zu/cse321a
Office hours: Sunday 1:00pm – 2:00pm

## Slide 3: Chapter 3. A Top-Level View of Computer Function and Interconnection (Cont.)

## Slide 4: Overview
Computer Structure (Components):
  CPU, Memory, I/O.
Computer Function:
  Instruction Fetch/Execute.
  Interrupts.
Interconnection Structure:
  Transfer between mem. & proc., i/o & proc. … etc.
Bus Interconnection:
  Bus structure: address, data, and control lines.
  Multiple-bus hierarchies.
  Elements of bus design.

## Slide 5: Transfer of Control via Interrupts

## Slide 6: Multiple Interrupts
Disable interrupts
  Processor will ignore further interrupts while processing one interrupt.
  Interrupts remain pending and are checked after first interrupt has been processed.
  Interrupts handled in sequence as they occur.
Define priorities
  Low priority interrupts can be interrupted by higher priority interrupts.
  When higher priority interrupt has been processed, processor returns to previous interrupt.

## Slide 7: Multiple Interrupts - Sequential
X
Disable processing further interrupts!
Y
Enable processing further interrupts!

## Slide 8: Multiple Interrupts – Nested
X
Y

## Slide 9: Multiple Interrupts – Nested (example)
Interrupt priorities: Printer (P): 2, Disk (D): 4, Communication line (C): 5
ISR execution: 10 units, Interrupt scenario: P @ t=10, C @ t=15, D @ t=20
User Program
Printer ISR
Communication ISR
Disk ISR
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
_______
t = 0
t = 10
t = 15
t = 25
t = 25
t = 35
t = 40
P
C
D

## Slide 10: Interconnection Structures
All computer components/modules must be connected.
Collection of paths connecting various modules is called: Interconnection Structures
Different type of connection is required for different type of module.
  CPU
  Memory
  Input/Output

## Slide 11: CPU Connection
Reads instructions and data
Writes out data (after processing)
Sends control signals to other units
Receives (& acts on) interrupts

## Slide 12: Memory Connection
Receives control signals.
  Read
  Write
Receives addresses (of locations).
Sends data (read operation).
Receives data (write operation).

## Slide 13: I/O Connection
Similar to memory from computer’s viewpoint.
Receives control signals from computer.
  e.g., read and write.
Receives addresses from computer
  e.g., port no. to identify peripheral.
Output
  Receives data from computer
  Sends data to peripheral
Input
  Receives data from peripheral
  Sends data to computer
Sends control signals to peripherals.
  I/o commands (e.g., spin disk).
Sends interrupt signals to computer
I/O Module
M Ports
Read
Write
Internal
Data
Internal
Data
Address
Interrupt
Signals
External
Data
External
Data
Control
Signals

## Slide 14: Types of Transfers
CPU to memory.
Memory to CPU.
CPU to I/O.
I/O to CPU.
I/O to memory.
Memory to I/O.
Direct Memory Access (DMA)

## Slide 15: Bus Interconnection
There are a number of possible interconnection systems.
Single and multiple Bus structures are most common.
Examples of a bus:
  Internal: PCI, SATA
  External: USB
  Internal/external: SCSI

## Slide 16: What is a Bus? (1)
A communication pathway connecting two or more devices.
Usually by broadcast.
Consists of multiple lines (each carries 1 bit)
  e.g. 32 lines are needed to transfer 32 bits of data in parallel.
Bus lines typically:
  carry address, data, and/or control information
  supply power (VCC, GND, … etc.)
Power lines may not be shown.

## Slide 17: What is a Bus? (2)
Data lines
  Carries data: Remember that there is no difference between “data” and “instruction” at this level!
  Width is a key determinant of performance: 8, 16, 32, 64 bit.
Address lines
  Identify the source or destination of data.
    e.g. CPU needs to read an instruction (data) from a given location in memory.
  Bus width determines maximum memory capacity of system.
    e.g. 8080 has 16 bit address bus giving 64k address space.
Control lines
  Control and timing information: memory read/write signal, interrupt request, clock signals

## Slide 18: Bus Interconnection Scheme

## Slide 19: Single Bus Problems
If great number of devices are connected to bus, performance will suffer. Why?
  Greater bus length  greater propagation delay  more time required for device coordination
  Aggregate data transfer demand approaches bus capacity  bus speed becomes a bottleneck.
To overcome this problem:
  Most systems use multiple buses laid out hierarchically.

## Slide 20: Traditional Bus Architecture

## Slide 21: High Performance Bus

## Slide 22: Elements of Bus Design
Bus Type
Method of Arbitration
Timing
Data Transfer Type

## Slide 23: Bus Types
Dedicated
  Functional: separate data & address lines.
  Physical: multiple buses connecting different subsets of modules.
Multiplexed
  Shared lines.
  Address valid or data valid control line.
  Advantages:
    fewer lines.
  Disadvantages
    More complex control.
    Lower performance.

## Slide 24: Bus Arbitration (I)
More than one module controlling the bus.
  e.g. CPU and DMA controller.
Only one module may control bus at a time.
Need a special h/w for arbitration.
Arbitration may be centralized or distributed.

## Slide 25: Bus Arbitration (II)
Centralized Arbitration
  Single hardware device controlling bus access
    Bus controller or arbiter.
  May be part of CPU or separate.
Distributed Arbitration
  Each module may claim the bus.
  Control logic on all modules.

## Slide 26: Timing
Coordination of events on bus.
Synchronous
  Events determined by clock signals.
  Clock line belongs to the control bus.
  A single 1-0 is a bus cycle.
  All devices can read clock line.
  Usually sync on leading edge.
  Usually a single cycle for an event.
Asynchronous
  Occurrence of one event on a bus follows and depends on the occurrence of a previous events.

## Slide 27: Synchronous Timing Diagram

## Slide 28: Asynchronous Timing Diagram - Read

## Slide 29: Asynchronous Timing Diagram - Write

## Slide 30: Data Transfer Type (I)
Reading

## Slide 31: Data Transfer Type (II)
Reading

## Slide 32: Reading Material
Stallings, Chapter 3:
  Pages 80 – 93