## Slide 1
CSE 321a
Computer Organization (1)
تنظيم الحاسبات (1)
3rd year, Computer Engineering
Fall 2017
Lecture #8
Dr. Hazem Ibrahim Shehata
Dept. of Computer & Systems Engineering
Credits to Dr. Ahmed Abdul-Monem Ahmed for the slides

## Slide 2: Administrivia
Assignment #2:
  Due: Thursday, Nov. 16, 2017
Midterm:
  New Date: Sunday, Nov. 19, 2017
  New Time: 12:30pm - 1:45pm
  Location: TBA!
  Coverage: lecture #1  lecture #6
Website: http://hshehata.github.io/courses/zu/cse321a/
Office hours: Sunday 1:00pm – 2:00pm

## Slide 3
Chapter 12. Instruction Sets: Characteristics and Functions (cont.)

## Slide 4: Outline
Machine Instruction Characteristics
  Elements of machine instructions, instruction representation, instruction types, number of addresses, instruction set design issues.
Types of Operands
  Addresses, numbers, characters, logical data
  Example: x86 data types
Types of Operations
  Data transfer, arithmetic, logical, conversion, input/output, system control, transfer of control.

## Slide 5: 4. Conversion
Instructions that change the format of data.
  e. g., convert from binary to BCD.
Example: Translate (TR) instruction in IBM System 390.
TR R1 (L), R2
  R1: starting address of source; L: number of bytes to be translated; R2: starting address of a table of 8-bit codes.
  Each byte of the source bytes is replaced by a table entry indexed by that byte.
162
s a m
IRA
EBCDIC
115
Translate
115
97
109
IRA
R1
EBCDIC
:
128
R2
:
148
:
162
:
TR R1 (3), R2
100+97
100+109
100+115
97
109
128
148
162
128
148
100
50
MVI R1, 50
MVI R2, 100

## Slide 6: 5. Input/Output
May be done using data movement instructions
  memory-mapped i/o
May be using specific i/o instructions
  isolated i/o
May be done by a separate controller
  DMA
Notes: 23

## Slide 7: 5. Input/Output – Common Operations
Notes: 23

## Slide 8: 6. System Control
Privileged instructions.
Executed only when the processor is in a certain privileged state
  e.g., ring 0, supervisor mode, kernel mode, ... etc.
Reserved for operating systems use.
Example Instructions:
  Modify storage protection keys.
  Access process control blocks (ID, address space, priority, … etc).
  …
Notes: 24

## Slide 9: 7. Transfer of Control
Most common transfer-of-control operations:
  branch, skip, and procedure call/return.
Branch (jump):
  Types: unconditional or conditional.
  Unconditional: always take the branch (update PC to equal address specified in operand).
    Ex.: BR X  branch to location X
  Conditional: take the branch if a condition is met, otherwise continue.
    Condition: test a flag set as a result of a recent operation, or perform a comparison (need three-address instruction)
      Ex.: BRP X  Branch to location X if result is positive.
      Ex.: BRE R1, R2, X  Branch to location X if [R1] equals [R2].
  Branches can be either forward or backward.
Notes: 25

## Slide 10: 7. Transfer of Control – Branch Instructions

## Slide 11: 7. Transfer of Control
Skip:
  Types: unconditional or conditional.
  Unconditional: always skip following instn. (update PC to equal address of following instn. plus ).
  Conditional: skip following instruction if condition is met, otherwise continue.
    Typical Example: increment-and-skip-if-zero (ISZ)
      301 …
      … …
      309 ISZ R1
      310 BR 301
      311 …
Notes: 25

## Slide 12: 7. Transfer of Control
Procedure call/return:
  Call: save address of following instruction (i.e., return address) and branch to target procedure.
    Return address can be saved: in special register, at start of called procedure, or on top of stack.
    Ex.: Call X  call the procedure at location X
  Return: Return to calling procedure.
    Load PC with the return address
    Ex.: Ret  return to where you came from!
  c.f. interrupt call/return
Register | Procedure Start | Stack Top
RN  [PC] PC  X | X  [PC] PC  X+1 | Push [PC] to stack PC  X
Register | Procedure Start | Stack Top
PC  [RN] | PC  [X] | Pop [PC] from stack
Notes: 25

## Slide 13: 7. Transfer of Control – Nested Procedure Calls

## Slide 14: Stack Frame Growth – Parameter Passing
Stack Pointer
Stack frame: set of (parameters + local variables + return address) necessary for a procedure call.
PUSH FP
MOV FP, SP
................
................
................
PUSH x1
PUSH x2
CALL Q
POP R0
POP T
POP FP
RETURN
PUSH FP
MOV FP, SP
...............
PUSH y1
PUSH y2
...............
Use FP to access x1, x2
...............
POP y2
POP y1
POP FP
RETURN
P
Q
Stack Pointer
Stack
Return Point [P]
Old Frame Pointer
x1
x2
Return Point [Q]
Old Frame Pointer
y1
y2
Stack Pointer
Stack Pointer
Frame Pointer
Stack Pointer
Stack Pointer
Frame Pointer
Stack Pointer
Stack Pointer

## Slide 15: 7. Transfer of Control – Common Op’s
Notes: 25

## Slide 16: Byte Order
In what order do we read numbers that occupy more than one byte? e.g. (numbers in hex) 12345678 can be stored in 4x8-bit locations as follows:
The problem is called Endian.
Highest significant byte in lowest address:
  Big-endian.
Least significant byte in lowest address:
  Little-endian.
Address
184
185
186
187
Value (1)
12
34
56
78
Value (2)
78
56
34
12
Big endian
Little endian
Notes: 27

## Slide 17: Example of C Data Structure

## Slide 18: Standard…What Standard?
X86 and VAX are little-endian.
IBM System 370/390, Sun SPARC, and most RISC are big-endian.
Big-endian is favored for:
  Character-string sorting: multiple bytes can be compared in parallel.
  Decimal/ASCII dumps: values can be printed left to right without causing confusion.
  Consistent order: integers and character strings are stored in the same order.
Little-endian is favored for:
  32-to-16-bit integer conversion: no need to increment address to access least-significant 2 bytes.
  Higher-precision arithmetic: no need to find the least-significant byte and move backward.
Notes: 30

## Slide 19: Reading Material
Stallings, Chapter 12:
  Pages 425 – 431
  Pages 447 – 450