## Slide 1: CSC 211 - Digital Logic Design 211 عال - تصميم المنطق الرقمي First Term - 1439/1440 Lecture #9
Dr. Hazem Ibrahim Shehata
Assistant Professor
College of Computing and Information Technology

## Slide 2: Administrivia
Assignment #2:
  To be released on Sunday.
Website: http://hshehata.github.io/courses/su/cs211

## Slide 3: Chapter 5: Combinational Logic Analysis

## Slide 4: Types of Digital Logic Circuits
There are two types of Digital Logic Circuits:
  Combinational Logic Circuits:
    Output is a pure function in the present inputs only!
    Examples: adders, subtractors, encoder, decoders, multiplexers, … etc.
  Sequential Logic Circuits:
    Output depends not only on the present input but also on the history of the input!!
    Examples: flip-flops, latches, registers, counters, memory, … etc.

## Slide 5: Implementing Combinational Logic
Methods for implementing Combinational Logic:
  AND-OR Logic
    Usage: implementing SOP and POS expressions
  NAND Logic
    Usage: implementing SOP expressions
  NOR Logic
    Usage: implementing POS expressions
  …

## Slide 6: Implementing SOP expressions using AND-OR Logic
Example: SOP  AND-OR logic
Each product term is implemented by an AND gate whose inputs are the literals of the product term.
All the outputs of the AND gates are fed to an OR gate.

## Slide 7: Implementing POS expressions using AND-OR Logic
Example: POS  AND-OR logic
Each sum term is implemented by an OR gate whose inputs are the literals of the product term.
All the outputs of the OR gates are fed to an AND gate.

## Slide 8: Universality of NAND gate
NAND gates can be used to implement all other gates: NOT, AND, OR, NOR!!
Hence, NAND gates can be used to implement any combinational circuit!!!

## Slide 9: Implementing SOP expressions using NAND Logic
Example: SOP  NAND logic
Start from the AND-OR implementation (like slide #7) and then replace each:
  Inverter  NAND gate (Connected inputs).
  AND  NAND
  OR  NAND

## Slide 10: Universality of NOR gate
NOR gates can be used to implement all other gates: NOT, AND, OR, NAND!!
Hence, NOR gates can be used to implement any combinational circuit!!!

## Slide 11: Implementing POS expressions using NOR Logic
Example: POS  AND-OR logic
Start from the AND-OR implementation (like slide #8) and then replace each:
  Inverter  NOR gate (Connected inputs).
  OR  NOR
  AND  NOR

## Slide 12: Implementing XOR Gate () using AND-OR Logic
1
2
3
4

## Slide 13: Implementing XNOR Gate () using AND-OR Logic
1
2
3

## Slide 14: Chapter 6: Functions of Combinational Logic

## Slide 15: The Half-Adder
A combinational logic circuit.
Purpose: adds two bits, by rules of binary addition:
Input/Output:
  Accepts two binary digits
  Produces a sum bit and a carry bit.
 | 0 |  |  |  | 0 |  |  |  | 1 |  |  |  | 1
+ | 0 |  |  | + | 1 |  |  | + | 0 |  |  | + | 1
 | 0 |  |  |  | 1 |  |  |  | 1 |  |  |  | 10

## Slide 16: Implementing the Half Adder
1
2
3
4

## Slide 17: The Full-Adder
A combinational logic circuit.
Purpose: adds three bits
Input/Output:
  Accepts two binary digits & input carry
  Produces a sum bit and a carry bit.

## Slide 18: Implementing the Full Adder
1
2
3

## Slide 19: Implementing the Full Adder
4
3

## Slide 20: Implementing the Full Adder
4

## Slide 21: Reading Material
Floyd, Chapter 5:
  Pages 234 – 235, 237, 239 – 248, 250, 252 – 255
Floyd, Chapter 6:
  Pages 285 - 289