## Slide 1
CSE 321b
Computer Organization (2)
تنظيم الحاسب (2)
3rd year, Computer Engineering
Winter 2017
Lecture #8
Dr. Hazem Ibrahim Shehata
Dept. of Computer & Systems Engineering
Credits to Dr. Ahmed Abdul-Monem Ahmed for the slides

## Slide 2: Adminstrivia
Assignment #2:
  Due: Thursday, April 13, 2017
Midterm:
  Date: Saturday, April 15, 2017
  Time: 10:30am – 12:00pm
  Location: classroom #27309
  Coverage: lectures #1  #6
Website: http://hshehata.github.io/courses/zu/cse321b/
Office hours: TBA

## Slide 3: Chapter 10. Computer Arithmetic (Cont.)

## Slide 4: Outline
Integer Representation
  Sign-Magnitude, Two’s Complement, Biased
Integer Arithmetic
  Negation, Addition, Subtraction
  Multiplication, Division
Floating-Point Representation
  IEEE 754
Floating-Point Arithmetic
  Addition, Subtraction
  Multiplication, Division
  Rounding

## Slide 5: Multiplication Example
Complex (relative to addition)!!
  Work out a partial product for each digit.
  Shift the partial product appropriately.
  Add partial products.
  Generate double-length result.
Running addition.
1  add & shift
0  shift only
المضروب
المضاعِف
الناتج

## Slide 6: Unsigned Binary Multiplication
Initially 0
Initially 0
Product

## Slide 7: Flowchart for Unsigned Binary Multiplication

## Slide 8: Execution of Example
Product (143)

## Slide 9: Signed Binary Multiplication
The straight forward multiplication algorithm doesn’t work with signed numbers!!
Evidence: In the previous example, suppose that M & Q are interpreted as signed numbers:
  M = (1011)2 which represents (-5)10
  Q = (1101)2 which represents (-3)10
  Applying the algorithm results in a product value of (1000 1111)2 which represents (-113)10
  This result is wrong! Correct value is supposed to be (+15)10!!!!

## Slide 10: Signed Multiplication Algorithm #1
Convert multiplicand (M) & multiplier (Q) to their absolute (positive) values |M| & |Q|.
Run the unsigned multiplication algorithm on |M| & |Q| to obtain the final product (P).
Adjust the sign of P (by 2’s complementation where needed) according to the following rule:
  sign(P) = sign(M) X sign(Q)

## Slide 11: Signed Multiplication Algorithm #2 (Booth’s Algorithm)
0 1 0 1 1 0 1
X 0 0 1 1 1 1 0
0 1 0 0 0 0 0
– 0 0 0 0 0 1 0
0 +1 0 0 0 –1 0
Multiplier
Multiplier

## Slide 12: Booth's Algorithm – Example
2’s complement of
the multiplicand

## Slide 13: Booth's Algorithm – Rule
Multiplier Bit i Bit i–1 | Version of multiplicand selected by bit i
0 0 | 0 × M
0 1 | +1 × M
1 0 | –1 × M
1 1 | 0 × M

## Slide 14: Booth’s Algorithm Flowchart

## Slide 15: Example on Booth’s Algorithm
Product (21)

## Slide 16: Booth's Algorithm, –ve Multiplier

## Slide 17: Booth’s Algorithm - Cases
Worst-case
Multiplier
0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
+1 | -1 | +1 | -1 | +1 | -1 | +1 | -1 | +1 | -1 | +1 | -1 | +1 | -1 | +1 | -1
Ordinary
Multiplier
1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0
0 | -1 | 0 | 0 | +1 | -1 | +1 | 0 | -1 | +1 | 0 | 0 | 0 | -1 | 0 | 0
Good
Multiplier
0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1
0 | 0 | +1 | 0 | 0 | 0 | 0 | -1 | 0 | 0 | 0 | 0 | +1 | 0 | 0 | -1
Booth’s Algorithm – Pros:
Treats +ve and –ve multipliers uniformly.
Use fewer additions if the multiplier has large blocks of 1’s.
On average, has the same efficiency as the normal algorithm.

## Slide 18: Division
More complex than multiplication.
Negative numbers are really bad!
Based on long division.
القاسم
المقسوم
الحاصل
الباقي

## Slide 19: Restoring Division (Positive Integers)
Quotient in Q
Remainder in A
An-1
A0
· · ·
Qn-1
Q0
· · ·
M0
· · ·
Mn-1
Dividend
Divisor
A←A–M
000…0
Quotient
Remainder
Restore

## Slide 20: Restoring Division Example
7/3
Quotient
Remainder
First cycle
Second cycle
Third cycle
Fourth cycle

## Slide 21: Non-Restoring Division (Positive Integers)
START
A ← 0
M ← Divisor
Q ← Dividend
Count ← n
A < 0 ?
Shift Left A,Q
A ← A + M
Shift Left A,Q
A ← A – M
Count = 0 ?
Q0 ← 1
Q0 ← 0
A ← A + M
A < 0 ?
END
Count ← Count – 1
A < 0 ?
Yes
No
Yes
No
No
Yes
Yes
No
Quotient in Q
Remainder in A

## Slide 22: Non-Restoring Division Example
A | Q |  | M = 0011
0000 | 0111 |  | Initial Values
0000 | 111? |  | Shift
1101 | 111? |  | Subtract
1101 | 1110 |  | Q0 ← 0
1011 | 110? |  | Shift
1110 | 110? |  | Add
1110 | 1100 |  | Q0 ← 0
1101 | 100? |  | Shift
0000 | 100? |  | Add
0000 | 1001 |  | Q0 ← 1
0001 | 001? |  | Shift
1110 | 001? |  | Subtract
1110 | 0010 |  | Q0 ← 0
0001 | 0010 |  | Add
First cycle
Second cycle
Third cycle
Fourth cycle
7/3
A | Q |  | M = 0011
0000 | 0111 |  | Initial Values
0000 | 111? |  | Shift
1101 | 111? |  | Subtract
1101 | 1110 |  | Q0 ← 0
1011 | 110? |  | Shift
1110 | 110? |  | Add
1110 | 1100 |  | Q0 ← 0
1101 | 100? |  | Shift
0000 | 100? |  | Add
0000 | 1001 |  | Q0 ← 1
0001 | 001? |  | Shift
1110 | 001? |  | Subtract
1110 | 0010 |  | Q0 ← 0
0001 | 0010 |  | Add
Remainder
Quotient

## Slide 23: Dealing with Signed Integers
Given a dividend (D) and divisor (V) where both are signed integers in the 2’s complement representation.
Division can be carried out as follows:
  Convert D & V to their absolute (+ve) values |D| & |V|.
  Run either restoring or non-restoring division on |D| & |V| to obtain the quotient (Q) and the remainder (R).
  Adjust the sign of Q and R (by 2’s complementation where needed) according to the following rules:
    sign(Q) = sign(D) X sign(V)
    sign(R) = sign(D)

## Slide 24: Reading Material
Stallings, Chapter 10:
  Pages 331 – 341