## Slide 1
CSE 321a
Computer Organization (1)
تنظيم الحاسبات (1)
3rd year, Computer Engineering
Fall 2017
Lecture #2
Dr. Hazem Ibrahim Shehata
Dept. of Computer & Systems Engineering
Credits to Dr. Ahmed Abdul-Monem Ahmed for the slides

## Slide 2: Administrivia
Website:
  http://hshehata.github.io/courses/zu/cse321a/
Lecture Day/Time:
  Tuesday 10:15am - 12:45am
Office Hours:
  TBA!
Tutorials:
  Started this week on Sunday at 2:55pm (just once!)
  Regular day/time: TBA!
Assignment #1:
  To be released early next week.
  Work in groups of two.

## Slide 3: Ch. 3: A Top-Level View of Computer Function and Interconnection

## Slide 4: Overview
Computer Structure (Components)
Computer Function
  Instruction Fetch and Execute
  Interrupts
Interconnection Structures
Bus Interconnection
  Bus Structure
  Multiple-Bus Hierarchies
  Elements of Bus Design

## Slide 5: Von Neumann (Princeton) Architecture
Almost all contemporary computer designs are based on three basic concepts introduced by John von Neumann in 1945:
Data and instructions are stored in a single read-write memory.
The contents of this memory are addressable by location, without regard to the type of data contained there.
Execution occurs in a sequential fashion (unless modified) from one instruction to the next.

## Slide 6: Program Concept
Using a fixed set of logic components, there are two ways to build a system that performs a specific computation on some input data:
  Special-purpose (customized) hardware:
    Logic components are connected and configured specifically to perform a particular computation.
    Type of computation is specified by way in which components are connected/configured  hardwired programming.
    To change computation, rewire components  inflexible!
  General-purpose hardware:
    Logic components are connected to form a general-purpose hardware that gets configured using set of input control signals.
    Type of computation (reflected by control signals values) is specified by sequence of input codes  software programming.
    To change computation, change code  flexible!

## Slide 7
Sequence of arithmetic and logic functions
Data
Results
Customized hardware
General-purpose arithmetic and logic functions
Data
Results
Instruction Interpreter
Instruction codes
Control signals
Programming in H/W
Programming in S/W
Each code is an instruction.
A sequence of codes (or instructions) is called software program.
CPU

## Slide 8: What is a program?
A sequence of steps.
For each step, an arithmetic or logical operation could be done.
For each operation, a different set of control signals are generated.
  Each operation is assigned a unique code.
    e.g., ADD  9D, MOVE  E3, … etc.
  A hardware segment accepts the code and issues the control signals.
That’s it. We have a computer!

## Slide 9: Computer Components
Each computer component takes some part in implementing the “s/w programming” approach:
  Control unit (CU) acts as instruction interpreter.
  Arithmetic and logic unit (ALU) implements general-purpose arithmetic and logic functions.
  Both CU and ALU constitute most of central processing unit (CPU).
  Data/code get into system, and results get out through input/output (I/O) units.
  Data, code, and results are stored temporarily while being processed in main memory (MM) unit.

## Slide 11: Overview
Computer Structure (Components)
Computer Function
  Instruction Fetch and Execute
  Interrupts
Interconnection Structures
Bus Interconnection
  Bus Structure
  Multiple-Bus Hierarchies
  Elements of Bus Design

## Slide 12: Instruction Cycle
Two steps:
  Fetch: CPU reads instructions from memory, one at a time.
  Execute: CPU executes instructions.

## Slide 13: Fetch Cycle
Program Counter (PC) holds address of next instruction to fetch.
Processor fetches instruction from memory location pointed to by PC.
Increment PC.
  Unless told otherwise
Instruction loaded into Instruction Register (IR).
Processor interprets instruction and performs required actions in execute cycle.

## Slide 14: Execute Cycle
Processor-memory
  Data transfer between CPU and main memory
Processor-I/O
  Data transfer between CPU and I/O module
Data processing
  Some arithmetic or logical operation on data
Control
  Alteration of sequence of operations
  e.g., jump
Combination of the above

## Slide 15: Hypothetical Machine
Address
Opcode
Instruction Format
0
3
4
15
Magnitude
S
0
1
15
Integer Format
Program Counter (PC)
Instruction Register (IR)
Accumulator (AC)
CPU Registers
0001 = Load AC from memory.
0010 = Store AC to memory.
0101 = Add to AC from memory.
Partial List of Opcodes

## Slide 16
First instruction
Second instruction
Third instruction
Fetch cycle
Execute cycle

## Slide 17: Instruction Cycle: State Diagram
CPU-memory or CPU-I/O operations
Internal CPU operations

## Slide 18: Overview
Computer Structure (Components)
Computer Function
  Instruction Fetch and Execute
  Interrupts
Interconnection Structures
Bus Interconnection
  Bus Structure
  Multiple-Bus Hierarchies
  Elements of Bus Design

## Slide 19: Interrupts
Interrupts are provided to improve processing efficiency.
Mechanism by which other modules (e.g. I/O) may interrupt normal sequence of processing
Most common classes of interrupts:
  Program
    e.g. overflow, division by zero
  Timer
    Generated by internal processor timer
    Used in pre-emptive multi-tasking (i.e., CPU time sharing).
  I/O
    From I/O controller
  Hardware failure
    e.g. memory parity error

## Slide 20: Transfer of Control via Interrupts

## Slide 21: Program Flow Control

## Slide 22: Program Timing

## Slide 23: Interrupt Cycle
Added to instruction cycle.
Processor checks for interrupt
  Indicated by an interrupt signal
If no interrupt:
  fetch next instruction
If interrupt pending:
  Suspend execution of current program.
  Save context (PC & relevant data).
  Set PC to start address of interrupt handler routine.
  Process interrupt.
  Restore context and continue interrupted program.

## Slide 24: Instruction Cycle (with interrupts)

## Slide 25: Instruction Cycle: State Diagram (with interrupts)

## Slide 26: Reading Material
Stallings, Chapter 3:
  Pages 66 – 80