## Slide 1
CSE 321b
Computer Organization (2)
تنظيم الحاسب (2)
3rd year, Computer Engineering
Winter 2017
Lecture #9
Dr. Hazem Ibrahim Shehata
Dept. of Computer & Systems Engineering
Credits to Dr. Ahmed Abdul-Monem Ahmed for the slides

## Slide 2: Adminstrivia
Midterm:
  New date: Wednesday, April 26, 2017
  New time: 10:30pm – 12:00pm
  Location: classroom #27309
  Coverage: lectures #1  #6
Assignment #2:
  Final due date: Sunday, April 23, 2017
Website: http://hshehata.github.io/courses/zu/cse321b/
Office hours: TBA

## Slide 3: Chapter 10. Computer Arithmetic (Cont.)

## Slide 4: Outline
Integer Representation
  Sign-Magnitude, Two’s Complement, Biased
Integer Arithmetic
  Negation, Addition, Subtraction
  Multiplication, Division
Floating-Point Representation
  IEEE 754
Floating-Point Arithmetic
  Addition, Subtraction
  Multiplication, Division
  Rounding

## Slide 5: Real Numbers
Numbers with fractions.
Could be done in pure binary
  1001.1010 = 23 + 20 +2-1 + 2-3 =9.625
Where is the binary point?
Fixed?
  Very large/small numbers cannot be represented.
    e.g., 0.0000001, 10000000000
  Fractional part of the quotient in dividing very large numbers will be lost.
Moving/floating?
  How do you show where it is?
  976,000,000,000,000 = 9.76 × 1014
  0.0000000000000976 = 9.76 × 10–14
Can do the same with binary numbers.
What do we need to store?
.
0 0 1 0 1 1 0 1 0 0 1 1 1 0 1 0

## Slide 6: Floating-Point Representation
The base 2 is the same for all numbers  need not be stored.
Number is stored in a binary word with 3 fields:
  Sign: +/–
  Significand S
  Exponent E
Normal number: most significant digit of the significand (mantissa) is nonzero  1 for base 2 (binary).
What number to store in the significand field?
  Normal form: 1.011 × 2–3 
There is an implicit 1 to the left of the binary point (normalized).
Exponent indicates place value (floating-point position).
Sign
Exponent
Significand (Mantissa)
±S × 2E
0 . 0 0 1 0 1 1
Store only 011 in the significand field!

## Slide 7: Floating-Point Representation Biased Exponent
k-bit unsigned exponent E’ ranges from to
  e.g., 8-bit exponent: 0 ≤ E’ ≤ 255
The stored exponent E’ is a biased exponent
  E’ = E + (2k–1–1)
  e.g., for 8-bit exponent, E’ = E + 127
  ≤ E ≤
Why?
  Nonnegative floating-point numbers can be treated as unsigned integers for comparison purposes.
  This is not true for 2’s comp. or sign-magnitude representations.
Sign
Exponent
Significand (Mantissa)
±S × 2E
Biased
Exponent
bias
2k–1
?
?
0
?
?
–127
128
0
255
–127
128

## Slide 8: Normalization
FP numbers are usually normalized.
  i.e., exponent is adjusted so that leading bit (MSB) of mantissa is non-zero, i.e., 1.
  c.f., Scientific notation where numbers are normalized to give a single digit before the decimal point, e.g. 3.123 x 103.
Since the MSB of mantissa is always 1, there is no need to store it!

## Slide 9: Floating-Point Examples
1.1010001 × 210100
Positive  sign bit = 0
E’ = E + 127 = 10100 + 1111111 = 10010011
Mantissa = 1010001 0000000000000000
0 10010011 10100010000000000000000
1717698.56
Negative  sign bit = 1
E’ = E + 127 = 10100 + 1111111 = 10010011
Mantissa = 1010001 0000000000000000
1 10010011 10100010000000000000000
Positive  sign bit = 0
E’ = E + 127 = –10100 + 1111111 = 01101011
Mantissa = 1010001 0000000000000000
0 01101011 10100010000000000000000
Sign
Biased
Exponent
Significand (Mantissa)
23 bits
8 bits
1.638125 × 220
-1.1010001 × 210100
-1717698.56
-1.638125 × 220
1.1010001 × 2-10100
…
1.638125 × 2-20

## Slide 10: FP Ranges (32-bit)
32-bit FP number, 8-bit exponent, 23-bit mantissa.
Largest +ve number
  Largest true exponent: 128
  Largest mantissa: 1 + (1 – 2–23)= 2 – 2–23
Smallest +ve number
  Smallest true exponent: –127
  Smallst mantissa: 1
Smallest –ve number
Largest –ve number
Accuracy
  The effect of changing LSB of mantissa.
  23-bit mantissa 2-23  1.2 x 10-7
  About 6 decimal places.
(2–2–23) × 2128
0.111…11
2–127
– (2–223) × 2128
–2–127

## Slide 11: Expressible Numbers (32-bit)

## Slide 12: Density of Floating Point Numbers
32-bit FP number  232 different values represented.
No more individual values are represented with floating-point numbers. Numbers are just spread out.
Numbers represented in the FP representation are not spaced evenly along the line number. Why?
Range-precision tradeoff
  More bits for exponent  wider range & less precision
  Reason: there is a fixed number of values that can be represented!
  To increase both range and precision  use more bits!!!

## Slide 13: IEEE 754
Standard for floating-point representation.
Adopted 1985 and revised 2008.
IEEE 754-2008 defines many FP formats for different purposes:

## Slide 14: IEEE 754 - Binary32/64/128 Formats
Binary32
(Single-precision)
Binary64
(Double-precision)
Binary128
(Quadruple-precision)

## Slide 15: IEEE 754 - Binary32/64/128 Interpretations
32
64
128

## Slide 16: IEEE 754 - Binary32/64/128 Parameters

## Slide 17: IEEE 754 - NaNs
NaN:
  Symbolic entity encoded in FP format
  Types: Signaling (sNaN) or Quiet (qNaN)
  Both types have the same format:
  F distinguishes between the two types:
    F=0xxxx..xx  sNaN, F=1xxxx..xx  qNaN
Signaling NaN:
  Signals an invalid operation exception whenever it appears as an operand. Ex.: uninitialized variables
Quite NaN:
  Propagates without signaling exceptions.
S= 0 or 1 | E= 1111…11 | F ≠ 0000..00

## Slide 18: IEEE 754 - Quiet NaN

## Slide 19: IEEE 754 - Effect of Subnormal Numbers

## Slide 20: FP Arithmetic +/-
Algorithm:
  Check for zeros.
  Align significands (adjusting exponents).
  Add or subtract significands.
  Normalize result.
  Round result.

## Slide 21: FP Addition & Subtraction Flowchart
1. Zero Check
2. Align
3. Add
4. Normalize
5. Round

## Slide 22: Reading Material
Stallings, Chapter 10:
  Pages 341-352
  Pages 356-358