## Slide 1
CSE 321b
Computer Organization (2)
تنظيم الحاسب (2)
3rd year, Computer Engineering
Winter 2017
Lecture #10
Dr. Hazem Ibrahim Shehata
Dept. of Computer & Systems Engineering
Credits to Dr. Ahmed Abdul-Monem Ahmed for the slides

## Slide 2: Adminstrivia
Assignment #3:
  To be released early next week
Website: http://hshehata.github.io/courses/zu/cse321b/
Office hours: Sunday 11:30am – 12:30pm

## Slide 3: Chapter 10. Computer Arithmetic (Cont.)

## Slide 4: Outline
Integer Representation
  Sign-Magnitude, Two’s Complement, Biased
Integer Arithmetic
  Negation, Addition, Subtraction
  Multiplication, Division
Floating-Point Representation
  IEEE 754
Floating-Point Arithmetic
  Addition, Subtraction
  Multiplication, Division
  Rounding

## Slide 5: FP Arithmetic +/-
Algorithm:
  Check for zeros (and other special cases, e.g., NaN).
  Align significands (adjusting exponents).
  Add or subtract significands.
  Normalize result.
  Round result.

## Slide 6: FP Arithmetic x/
Algorithm:
  Check for zeros (and other special cases, e.g., NaN).
  Add/subtract exponents.
  Multiply/divide significands (watch sign).
  Normalize result.
  Round result.
All intermediate results should be in double length storage.

## Slide 7: Floating Point Multiplication

## Slide 8: Floating Point Division
∞

## Slide 9: Guard Bits
Extra bits added to the right of the mantissa during intermediate calculations.
Maintains good precision.
1 . 0 0 0 … 0 0 × 21
– 1 . 1 1 1 … 1 1 × 20
1 . 0 0 0 … 0 0 × 21
– 0 . 1 1 1 … 1 1 × 21
1 . 0 0 0 … 0 0 0 0 0 0 × 21
– 1 . 1 1 1 … 1 1 0 0 0 0 × 20
1 . 0 0 0 … 0 0 0 0 0 0 × 21
– 0 . 1 1 1 … 1 1 1 0 0 0 × 21
0 . 0 0 0 … 0 1 × 21
= 2–23 × 21 = 2–22
0 . 0 0 0 … 0 0 1 0 0 0 × 21
= 2–24 × 21 = 2–23

## Slide 10: Rounding
The result of any operation on significands is stored in a longer register.
When the result is to be stored as an FP number, extra bits have to be dropped off  rounding.
Round to nearest representable number.
Round toward +∞: round up to the next number.
  Ex.: +1.1…001 001  +1.1…010
  Ex.: – 1.1…001 001  – 1.1…001
Round toward –∞: round down to the next number.
  Ex.: +1.1…001 001  +1.1…001
  Ex.: – 1.1…001 001  – 1.1…010
Round toward zero: truncate the extra bits.
  Ex.: +1.1…001 001  +1.1…001
  Ex.: – 1.1…001 001  – 1.1…001

## Slide 11: Round to Nearest
Default technique listed in the IEEE standard.
Deliver the representable value nearest to the infinitely precise result. If the two nearest representable values are equally near, the one with LSB 0 will be delivered.
Examples:
  If the guard bits are 10010  they amount to more than one half of the last representable bit position  Round away from zero.
  If the guard bits are 01111  they amount to less than one half of the last representable bit position  Truncate.
  If the guard bits are 10000  midway
    If we always truncate  biased toward zero.
    If we choose randomly  not predictable/deterministic results.
    IEEE standard:
      Force the result to be even.
      If last bit is 1, round away from zero, else, truncate.

## Slide 12: Round to ±∞
Useful in implementing interval arithmetic.
Interval arithmetic: produce two values for every result. These two values correspond to the lower and upper endpoints of an interval that contains the true result.
Used in monitoring and controlling errors.

## Slide 13: Reading Material
Stallings, Chapter 10:
  Pages 352-356