## Slide 1
CSE 321a
Computer Organization (1)
تنظيم الحاسبات (1)
3rd year, Computer Engineering
Fall 2017
Lecture #10
Dr. Hazem Ibrahim Shehata
Dept. of Computer & Systems Engineering
Credits to Dr. Ahmed Abdul-Monem Ahmed for the slides

## Slide 2: Administrivia
Midterm:
  Marks have been posted.
Assignment #3:
  To be released by next week.
Website: http://hshehata.github.io/courses/zu/cse321a
Office hours: Sunday 1:00pm-2:00pm

## Slide 3: Chapter 19. Control Unit Operation (Online Appendix)

## Slide 4
Sequence of arithmetic and logic functions
Data
Results
Customized hardware
General-purpose arithmetic and logic functions
Data
Results
Instruction Interpreter
Instruction codes
Control signals
Programming in H/W
Programming in S/W
Each code is an instruction.
A sequence of codes (or instructions) is called software.
CPU

## Slide 5: Micro-operations
A computer executes programs.
A program is a sequence of instructions  instruction cycles.
Each instruction is made up of smaller units (subcycles).
  e.g., fetch/execute subcycles.
Each subcycle has a number of steps.
Each step has a number of micro-operations.
Each micro-operation does very little.
Micro-operation is an atomic operation of CPU.
Any instruction is a sequence of micro-operations.

## Slide 6: Constituent Elements of Prog. Execution
step
step
step
step

## Slide 7: Fetch Subcycle in simple machine
0000000001100100
0001000000100000
0000000011001000
0001101001101000
MAR
MBR
PC
IR
AC
Memory Address Register (MAR)
  Specifies address for read or write operation.
  Connected to address bus.
Memory Buffer Register (MBR)
  Holds data to write or last data read.
  Connected to data bus.
Program Counter (PC)
  Holds address of next instruction to be fetched.
Instruction Register (IR)
  Holds last instruction fetched (being executed).
Accumulator (AC)
  Acts as implicit operand.

## Slide 8: Fetch Sequence
Address of next instruction is in PC.
Address in PC is copied to MAR.
Memory location (pointed to by MAR) is read to MBR.
  Address in MAR is placed on address bus.
  Control unit issues READ command.
  Result (data from memory) appears on data bus.
  Data from data bus is copied into MBR.
PC is incremented by 1 (in parallel with data fetch from memory).
Data (instruction) is moved from MBR to IR.
MBR is now free for further data fetches.

## Slide 9: Fetch Subcycle (symbolic)
t1: MAR ← [PC]
t2: MBR ← Memory,
PC ← [PC] + I
t3: IR ← [MBR]
(tx = time unit/clock cycle)
Micro-operations take equal times.
Or
t1: MAR ← [PC]
t2: MBR ← Memory
t3: PC ← [PC] + l,
IR ← [MBR]
Step
Micro-operation
t1
t2
t3

## Slide 10: Rules for Clock Cycle Grouping
Proper sequence must be followed
  MAR ← [PC] must precede MBR ← Memory
Read/write conflicts must be avoided
  A µop reading from reg. X cannot be scheduled at the same step (cycle) with another µop writing to reg. X.
    Ex.: MBR ← Memory & IR ← [MBR] must not be in same step.
Resource conflicts must be avoided
  For instance, 2 µop’s involving addition cannot be scheduled at the same step if ALU contains 1 adder only.
  Note: PC ← [PC] + l involves addition, and hence use ALU.

## Slide 11: Indirect Subcycle
t1: MAR ← [IR-address] - address field of IR
t2: MBR ← Memory
t3: IR-address ← [MBR]
MBR contains an address.
IR is now in same state as if direct addressing had been used.

## Slide 12: Interrupt Subcycle
At the end of the execute subcycle, interrupts are tested.
Some interrupt occurred  interrupt subcycle.
Assume: address of ISR routine & address of location to save PC become available in the second step.
t1: MBR ← [PC]
t2: MAR ← save-address, PC ← routine-address
t3: Memory ← [MBR]
This is a minimum
  May be additional micro-ops to get addresses.
  N.B. saving context is done by interrupt handler routine, not micro-ops.

## Slide 13: Execute Subcycle (ADD)
Execute subcycle is different for each instruction.
ADD X
  Add contents of location X to AC and save result to AC
t1: MAR ← [IR-address]
t2: MBR ← Memory
t3: AC ← [AC] + [MBR]
Note no overlap of micro-operations.

## Slide 14: Execute Subcycle (ISZ)
ISZ X - increment and skip if zero
  t1: MAR ← [IR-address]
  t2: MBR ← Memory
  t3: MBR ← [MBR] + 1
  t4: Memory ← [MBR]
  if [MBR] == 0 then PC ← [PC] + 1
Notes:
  “If …” is a single micro-operation.
  Micro-operations done during t4.

## Slide 15: Execute Subcycle (BSA)
BSA X - Branch and save address
  Address of instruction following BSA is saved in X
  Execution continues from X+1
  t1: MAR ← [IR-address], MBR ← [PC]
  t2: PC ← [IR-address], Memory ← [MBR]
  t3: PC ← [PC] + 1

## Slide 16: Instruction Cycle – Flowchart
01

## Slide 17: Model of the Control Unit

## Slide 18: Control Unit – Inputs and Outputs
Inputs
  Clock:
    One micro-operation (or set of parallel micro-operations) per clock cycle.
  Instruction register
    Opcode for current instruction.
    Determines which micro-operations are performed.
  Flags
    State of CPU.
    Results of previous operations.
  Control signals from control bus
    Interrupts.
    Acknowledgements.
Outputs (control signals)
  Within CPU
    Causes data movement.
    Activates specific functions.
  Via control bus: to memory and to I/O modules.

## Slide 19: Data Paths and Control Signals
MAR ← [PC]
  - Control unit activates signal to open gates between PC and MAR: C2
MBR ← Memory
  - Open gates between MAR and address bus : C0
  - Memory read control signal.: CR
  - Open gates between data bus and MBR : C5
Instruction Fetch
C14

## Slide 20
Micro-operations | Timing | Active Control Signals
Fetch: | t1: MAR  [PC] | C2
 | t2: MBR  Memory PC  [PC] +1 | C0, CR,C5
 | t3: IR  [MBR] | C4
Indirect: | t1: MAR  [IR-address] | C14
 | t2: MBR  Memory | C0, CR, C5
 | t3: IR-address  [MBR] | C4
Interrupt: | t1: MBR  [PC] | C1
 | t2: MAR  Save-address PC  Routine-address | 
 | t3: Memory  [MBR] | C0, CW, C12
CR: Read control signal to system bus. CW: Write control signal to system bus. |  | 

## Slide 21: Internal Organization
Usually a single internal bus.
Gates control movement of data onto and off the bus.
Control signals control data transfer to and from external systems bus.
Temporary registers needed for proper operation of ALU.
Example: ADD X
t1: MAR ← [IR-address]
t2: MBR ← Memory
Y ← [AC]
t3: Z ← [MBR] + [Y]
t4: AC ← [Z]
ALU

## Slide 22: Implementing the Control Unit
A wide variety of techniques have been used.
Most of them fall into one of two categories:
  Hardwired implementation
    Control signals are generated by a state machine circuit.
  Microprogrammed implementation
    Control signals are generated by a program similar to machine language programs.

## Slide 23: Hardwired Implementation
Control
Unit
ICC
P
Q
Core
Logic

## Slide 24: Control Unit Core
To design the core logic, we need to derive a Boolean expression for each control signal.
Example: let’s derive an expression for C5 (read data from external bus to MBR)
  Suppose instruction subcycles are encoded by control signals P & Q s.t. PQ=00  Fetch, PQ=01  Indirect, PQ=10  Execute, PQ=11  Interrupt.
  Suppose C5 should be activated in:
    Step 2 (T2) during fetch and indirect subcycles.
    Step 3 (T3) during execution of ADD (I5) and AND (I8) instructions.
  Boolean expression for C5:

## Slide 25: Problems with Hardwired Design
Complex sequencing & micro-operation logic.
Difficult to design and test.
Inflexible design.
  Difficult to add new instructions.

## Slide 26: Reading Material
Stallings, Chapter 19:
  URL: http://www.ecs.csun.edu/~cputnam/Comp546/Stallings-Appendices/19-Control_Unit.pdf
  Pages 1 – 24
  Pages 30 – 35