## Slide 1
CSE 321a
Computer Organization (1)
تنظيم الحاسبات (1)
3rd year, Computer Engineering
Fall 2016
Lecture #5
Dr. Hazem Ibrahim Shehata
Dept. of Computer & Systems Engineering
Credits to Dr. Ahmed Abdul-Monem Ahmed for the slides

## Slide 2: Administrivia
Lecture:
  Will get back to regular schedule starting next week!
  Day/Time: Tuesday, 10:15am – 12:45pm
Assignment #1:
  Solution will posted on Thursday.
Website: http://hshehata.github.io/courses/zu/cse321a
Office hours: Sunday 12:00pm-1:00pm

## Slide 3: Chapter 4. Cache Memory (cont.)

## Slide 4: Cache Memory - Concept
One-Level Cached
Memory System
Three-Level Cached
Memory System

## Slide 5: Cache Memory – Design
Mapping function
Replacement algorithm
Read/Write policies
Number of caches
Addresses
Size
Block/line size

## Slide 6: Cache Memory – Design
Mapping function
Replacement algorithm
Read/Write policies
Number of caches
Addresses
Size
Block/line size

## Slide 7: (I) Direct Mapping
Block 0
Block 1
Block 2
Block m-1
. . .
. . .
Block m
Block m+1
Block 2m-1
. . .
. . .
Block M-m
Block M-1
. . .
. . .
Block M-m+1
Block M-m+2
. . .
. . .
. . .
Line 0
Line 1
Line 2
Line m-1
Main Memory
Cache Memory
Block m+2
Each MM block maps to only one cache line.
Block #b maps to line #(b modulo m).
If a block is in cache, it must be in one specific place.

## Slide 8: (I) Direct Mapping Cache Line Table
Cache line # (b modulo m) | MM block # (b)
0
0, m, 2m, 3m, …, M-m
1
1,m+1, 2m+1, …, M-m+1
m-1
m-1, 2m-1, 3m-1, …, M-1
……
………………………….
2
2,m+2, 2m+2, …, M-m+2
Number of MM blocks = M
Number of cache lines = m






## Slide 9: (I) Direct Mapping Tiny Example
Main memory:
  1 Location ≡ 1 word ≡ 1 byte
  32 byte
    Length of address = log2 32 = 5
  4-byte blocks
    # of blocks (M) = 32 / 4 = 8
Cache:
  16 byte
  4-bytes lines
    # of lines (m) = 16 / 4 = 4

## Slide 10: (I) Direct Mapping Tiny Example
 | 00000
 | 00001
 | 00010
 | 00011
 | 00100
 | 00101
 | 00110
 | 00111
 | 01000
 | 01001
 | 01010
 | 01011
 | 01100
 | 01101
 | 01110
 | 01111
 | 10000
 | 10001
 | 10010
 | 10011
 | 10100
 | 10101
 | 10110
 | 10111
 | 11000
 | 11001
 | 11010
 | 11011
 | 11100
 | 11101
 | 11110
 | 11111
B0
B2
B4
B6
B1
B3
B5
B7
L0
L2
L1
L3
Main Memory
Cache Memory
001 tag=0, line=01
010 tag=0, line=10
110: tag=1, line=10
101 tag=1, line=01
Block # |  | Word #
1 | 01 | 10
Tag # | Line # | 

## Slide 11: (I) Direct Mapping Address Format
Memory address is split (based on block size) into:
  Least significant w bits  identify word in block.
    w = log2 (# of words in block).
  Most significant s bits  identify block in MM.
    s = log2 (# of blocks in MM).
    The s bits are split (based on cache size) into:
      Least significant r bits  identify cache line.
        r = log2 (# of lines in cache).
      Most significant s – r bits  tag (identify group).
In the “tiny example”: w=2, s=3, r=2, s-r=1.
Tag # (s-r bits)
Line # (r bits)
Word #
(w bits)
Block # (s bits)

## Slide 12: (I) Direct Mapping Big Example
Main memory:
  1 Location ≡ 1 word ≡ 1 byte
  16M byte
    Length of address = log2 16M = 24
  4-byte blocks
    # of blocks (M) = 16M / 4 = 4M
Cache:
  64K byte
  4-bytes lines
    # of lines (m) = 64K / 4 = 16K

## Slide 13: (I) Direct Mapping Big Example – Address Format
24-bit address
  s + w = (s-r) + r + w = 24
4-byte block  4M-block MM
  w = log2 4 = 2 bits
  s = 24 – w = 22 bits (Another way: s = log2 4M = 22 bits)
64K-byte Cache  16K-line Cache
  r = log2 16K = 14 bits
  s-r = 22 – 14 = 8 bits
Notes:
  No 2 blocks that map to the same line have the same tag field
  Check contents of cache by finding line and checking tag
Tag # (s-r bits)
Line # (r bits)
Word #
(w bits)
Block # (s bits)
2
22
14
8

## Slide 14: (I) Direct Mapping Address Format Summary
Address length = (s + w) bits.
Number of addressable units = 2s+w words.
Block size = line size = 2w words.
  w = log2 (# of words in block).
Number of blocks in MM = M = 2s+w/2w = 2s.
  s = log2 (# of words in MM / # of words in block)
Number of lines in cache = m = 2r.
  r = log2 (# of words in cache / # of words in line).
Size of tag = (s – r) bits.
  (s-r) = log2 (# of words in MM / # of words in cache)

## Slide 15: (I) Direct Mapping Cache Organization

## Slide 16: (I) Direct Mapping Big Example – Search
Main memory size = 16 MB
Cache size = 64 kB
Block size = 4 bytes
w = 2, r = 14, s-r = 8
(16339C)16 =
0001 0110 0011 0011 1001 1100
word
0CE7
Line
Tag

## Slide 17: (I) Direct Mapping Pros & Cons
Simple.
Inexpensive.
Fixed location for given block.
  If a program accesses 2 blocks that map to the same line repeatedly, cache misses are very high.

## Slide 18: (II) (Fully-)Associative Mapping
A main memory block can load into any line of cache.
Memory address is interpreted as tag and word.
Tag uniquely identifies block of memory.
Every line’s tag is examined for a match.
Cache searching gets expensive.

## Slide 19: (II) Associative Mapping Tiny Example
Main memory:
  1 Location ≡ 1 word ≡ 1 byte
  32 byte
    Length of address = log2 32 = 5
  4-byte blocks
    # of blocks (M) = 32 / 4 = 8
Cache:
  16 byte
  4-bytes lines
    # of lines (m) = 16 / 4 = 4

## Slide 20: (II) Associative Mapping Tiny Example
 | 00000
 | 00001
 | 00010
 | 00011
 | 00100
 | 00101
 | 00110
 | 00111
 | 01000
 | 01001
 | 01010
 | 01011
 | 01100
 | 01101
 | 01110
 | 01111
 | 10000
 | 10001
 | 10010
 | 10011
 | 10100
 | 10101
 | 10110
 | 10111
 | 11000
 | 11001
 | 11010
 | 11011
 | 11100
 | 11101
 | 11110
 | 11111
B0
B2
B4
B6
B1
B3
B5
B7
L0
L2
L1
L3
Main Memory
Cache Memory
000  tag=000
111 tag=111
101 tag=101
Block # | Word #
101 | 10
Tag # | 

## Slide 21: (II) Associative Mapping Address Format
Memory address is split (based on block size) into:
  Least significant w bits  identify word in block.
    w = log2 (# of words in block).
  Most significant s bits  identify block in MM, and used as a tag.
    s = log2 (# of blocks in MM).
In the “tiny example”: w=2, s=3.
Word #
(w bits)
Tag #
(s bits)

## Slide 22: (II) Associative Mapping Big Example
Main memory:
  1 Location ≡ 1 word ≡ 1 byte
  16M byte
    Length of address = log2 16M = 24
  4-byte blocks
    # of blocks (M) = 16M / 4 = 4M
Cache:
  64K byte
  4-bytes lines
    # of lines (m) = 64K / 4 = 16K

## Slide 23: (II) Associative Mapping Big Example – Address Format
24-bit address
  s + w = (s-r) + r + w = 24
4-byte block  4M-block cache
  w = log2 4 = 2 bits
  s = 24 – w = 22 bits (Another way: s = log2 4M = 22 bits)
Note:
  Each cache line can store a 4-byte block and a 22-bit tag (identifying that block).
  To find a block in cache, compare the address tag field (s) against all cache line tags until hit!!
2
22
Word #
(w bits)
Tag #
(s bits)

## Slide 24: (II) Associative Mapping Address Format Summary
Address length = (s + w) bits.
Number of addressable units = 2s+w words.
Block size = line size = 2w words.
  w = log2 (# of words in block).
Number of blocks in MM = M = 2s+w/2w = 2s.
  s = log2 (# of words in MM / # of words in block)
Number of lines in cache = m  unknown!
Size of tag = s.

## Slide 25: (II) Associative Mapping Cache Organization

## Slide 26: (II) Associative Mapping Big Example – Search
Main memory size = 16 MB
Cache size = 64 kB
Block size = 4 bytes
w = 2, s = 22
(16339C)16 =
0001 0110 0011 0011 1001 1100
word
058CE7
Tag

## Slide 27: (III) Set-Associative Mapping
Cache is divided into a number of sets (v) of equal size.
Each set contains a number of lines (k).
  k-way set-associative mapping!
A block b could map to any line in a set i if and only if i = b modulo v.

## Slide 28: (III) Set-Associative Mapping
Block 0
Block 1
Block 2
Block v-1
. . .
. . .
Block v
Block v+1
Block 2v-1
. . .
. . .
Block M-v
Block M-1
. . .
. . .
Block M-v+1
Block M-v+2
. . .
. . .
. . .
Main Memory
Cache Memory
Block v+2
Set 0
Set 1
Set 2
Set v-1
………….......
………….......
………….......
4-way set associative mapping

## Slide 29: (III) Set-Associative Mapping Tiny Example
Main memory:
  1 Location ≡ 1 word ≡ 1 byte
  32 byte
    Length of address = log2 32 = 5
  4-byte blocks
    # of blocks (M) = 32 / 4 = 8
Cache:
  16 byte
  4-bytes lines
    # of lines (m) = 16 / 4 = 4
  2-line sets  k=2  2-way set-associative
    # of sets (v) = 4 / 2 = 2

## Slide 30: (III) Set-Associative Mapping Tiny Example
 | 00000
 | 00001
 | 00010
 | 00011
 | 00100
 | 00101
 | 00110
 | 00111
 | 01000
 | 01001
 | 01010
 | 01011
 | 01100
 | 01101
 | 01110
 | 01111
 | 10000
 | 10001
 | 10010
 | 10011
 | 10100
 | 10101
 | 10110
 | 10111
 | 11000
 | 11001
 | 11010
 | 11011
 | 11100
 | 11101
 | 11110
 | 11111
B0
B2
B4
B6
B1
B3
B5
B7
L0
L2
L1
L3
Main Memory
Cache Memory
001 tag= 00, set=1
101 tag= 10, set= 1
Block # |  | Word #
10 | 1 | 10
Tag # | Set # | 
S0
S1
111 tag=11, set=1
011 tag= 01, set=1

## Slide 31: (III) Set-Associative Mapping Address Format
Memory address is split (based on block size) into:
  Least significant w bits  identify word in block.
    w = log2 (# of words in block).
  Most significant s bits  identify block in MM.
    s = log2 (# of blocks in MM).
    The s bits are split (based on cache size) into:
      Least significant d bits  identify cache set.
        d= log2 (# of sets in cache).
      Most significant s – d bits  tag (identify group).
In the “tiny example”: w=2, s=3, d=1, s-d=2.
Tag # (s-d bits)
Set # (d bits)
Word #
(w bits)
Block # (s bits)

## Slide 32: (III) Set-Associative Mapping Big Example
Main memory:
  1 Location ≡ 1 word ≡ 1 byte
  16M byte
    Length of address = log2 16M = 24
  4-byte blocks
    # of blocks (M) = 16M / 4 = 4M
Cache:
  64K byte
  4-bytes lines
    # of lines (m) = 64K / 4 = 16K
  2-line sets  k=2  2-way set-associative
    # of sets (v) = 16K / 2 = 8K

## Slide 33: (III) Set-Associative Mapping Big Example – Address Format
24-bit address
  s + w = (s-r) + r + w = 24
4-byte block
  w = log2 4 = 2 bits
  s = 24 – w = 22 bits
64K-byte Cache  16K-line Cache  8K-set Cache
  d = log2 8K = 13 bits
  s-r = 22 – 13 = 9 bits
Tag # (s-d bits)
Set # (d bits)
Word #
(w bits)
Block # (s bits)
2
22
13
9

## Slide 34: (III) Set-Associative Mapping Address Format Summary
Address length = (s + w) bits.
Number of addressable units = 2s+w words.
Block size = line size = 2w words.
  w = log2 (# of words in block).
Number of blocks in MM = M = 2s+w/2w = 2s.
  s = log2 (# of words in MM / # of words in block)
Number of lines in set = k  k-way set-associative
Number of sets = v = 2d.
Number of lines in cache = m = k * v = k * 2d.
  d = log2 (# of words in cache / # of words in set).
Size of tag = (s – d) bits.
  (s-d) = log2 (# of blocks in MM / # of sets in cache).

## Slide 35: (III) Set-Associative Mapping Cache Organization (k-way)
s+w

## Slide 36: (III) Set-Associative Mapping Big Example – Search
Main memory size = 16 MB
Cache size = 64 kB
Block size = 4 bytes
2-way set-associative mapping
w = 2, d = 13, s-d = 9

## Slide 37: Reading Material
Stallings, Chapter 4:
  Pages 123 – 136